## Slide 1: Cold Lightweight Imagers For Europa (C-LIFE)
Due to observed plumes, the Europan surface is a means to investigate its ocean…
…but the Europan Surface is a hostile location
Shane Byrne – University of Arizona (shane@LPL.arizona.edu)
Christian d'Aubigny, Bashar Rizk, Linda Powers, Michael Ward, Alyssa Baller, Steve Meyer, Elizabeth Turtle, Alfred McEwen
Our Camera Design Overcomes Five Major Challenges
      Radiation
      Planetary Protection
      Low Ambient Temperature
      Low Available Energy
      Very Low Downlink

## Slide 2
Radiation & Planetary Protection:
Dual-periscope design
maximizes self-shielding
Parts survive required thermal sterilization and radiation doses
Detector periscopes,
20cm apart
LED periscopes
Rad-hard Lens stack
Detector Readout Modules
Low Temperatures & Energy:
No moving parts or deployable covers with progressive focus and strip filters Cryogenic storage and no survival heating between observing sessions
Stereo in Pan
Fluorescence excited by three separate LEDs and detected by one notch filter
Color filters match the camera on Europa Clipper
Low Downlink:
Multi-image median filtering and wavelet compression. More-advanced tools in future work.
Redundant Electronics

## Slide 3: Cold Lightweight Imagers For Europa (C-LIFE)
Shane Byrne – University of Arizona (shane@LPL.arizona.edu)
Christian d'Aubigny, Bashar Rizk, Linda Powers, Michael Ward, Alyssa Baller, Steve Meyer, Elizabeth Turtle, Alfred McEwen
C-LIFE has high impact on mission success and Europan science.
Color stereo panorama
Fluorescence of organic materials in three bands
Plume detection through forward scattered light near east/west horizon
Change detection at excavation site and through tidal effects
Autonomous operation, higher-level product generation and smart algorithms to prioritize downlink