## Slide 1: Cold Lightweight Imagers For Europa (C-LIFE)
Shane Byrne – University of Arizona
Christian d'Aubigny, Bashar Rizk, Linda Powers, Michael Ward, Alyssa Baller, Steve Meyer, Elizabeth Turtle, Alfred McEwen

## Slide 2: Cold Lightweight Imagers For Europa (C-LIFE)
Due to observed plumes, the Europan surface is a means to investigate the ocean
Shane Byrne – shane@LPL.arizona.edu

## Slide 3: Cold Lightweight Imagers For Europa (C-LIFE)
The Europa Lander
  Focused on astrobiology
  One of the most hostile environments in the solar system
  An SDT defined three science goals, with many Objectives
Shane Byrne – shane@LPL.arizona.edu
Objectives Relevant to the Camera Instrument

## Slide 4: Cold Lightweight Imagers For Europa (C-LIFE)
The C-LIFE Camera is developed at U. Arizona under awards from NASA’s COLDTech and ICEE-2 programs
Industry Partners
  SRI International
  Ball Aerospace
  Space Dynamics Lab
Main Challenges
Radiation (mostly electrons)
Temperature (surface of Europa close to 100 K)
Planetary Protection (Camera Head must survive a 6-log reduction in bioburden)
Low available energy (a battery powered mission)
Very low downlink (600 Mbits for all science data)
Shane Byrne – shane@LPL.arizona.edu

## Slide 5: Cold Lightweight Imagers For Europa (C-LIFE)
C-LIFE ‘Traditional’ Science Plans
Europan day 1: Full color stereo panorama (needed early for sample site selection)
Europan day 2: Night-time fluorescence investigations and plume searches close to 6AM and 6PM (highest phase angles).
Europan day 3: Full color stereo of lander workspace assuming sampling activities have already occurred.
Europan day 4 & 5: Continued imaging for change detection of excavated material and from tidal responses.
…but 600 Mbit is a non-traditional constraint
Significant automation and onboard data processing will be necessary and something we’ll focus on in the upcoming year
Shane Byrne – shane@LPL.arizona.edu

## Slide 6: Cold Lightweight Imagers For Europa (C-LIFE)
C-LIFE architecture
Stereo Color Imager
Pan/Tilt from the HGA
No Moving Parts
No deployable lens covers
No Survival Heating
LEDs support nighttime and shadow imaging
Fluorescence investigation to find organics
A camera head with minimal electronics
Vault electronics with data processing and automation capabilities
Stereo in Pan
Fluorescence excited by three separate LEDs, but detected by one filter
Color filters match the camera on Europa Clipper
Progressive focus from infinity at the top of the detector to lander sample port at bottom
Shane Byrne – shane@LPL.arizona.edu

## Slide 7: Cold Lightweight Imagers For Europa (C-LIFE)
C-LIFE Camera head
24.5 x 9.5 x 6 cm, slim design
Dual periscope design shields detectors and LEDs from open space and provide maximum self-shielding
Two Detector Readout Modules from SRI utilize their MkxNk detector (1x2k)
Detector periscopes,
20cm apart
LED periscopes
Rad-hard Lens stack
Detector Readout Modules
Shane Byrne – shane@LPL.arizona.edu

## Slide 8: Cold Lightweight Imagers For Europa (C-LIFE)
Detector Readout Module
LED periscopes
Shane Byrne – shane@LPL.arizona.edu

## Slide 9: Cold Lightweight Imagers For Europa (C-LIFE)
C-LIFE is mission critical and so must be highly redundant.
Redundant Vault Electronics
Both Eyes
Cross-strapped
Shane Byrne – shane@LPL.arizona.edu

## Slide 10: Cold Lightweight Imagers For Europa (C-LIFE)
  Multi-image median filters
  Sub-setting and thumbnailing of images
  Wavelet compression
Future Investigations
  On board mosaic building
  On board stereo DTM generation
  Autonomous designation of most-typical and most-unusual terrain in surroundings
Shane Byrne – shane@LPL.arizona.edu
Vault Electronics are designed for low data return and high radiation.

## Slide 11: Cold Lightweight Imagers For Europa (C-LIFE)
Main challenges: Radiation
  NOVICE modeling performed by Ball Aerospace
  With our design, most parts tolerate the environment with an RDF of 2
  A few parts need more analysis – radiation test plan developed
Main challenges: Temperature
  ConOPs envisioning warming the Camera Head electronics only for a short operations period each Europan day.
  Cryogenic storage (no survival heating when not in use)
  UA and SDL testing program has established that all parts survive cryogenic storage for 10s of hours with no loss of performance
Shane Byrne – shane@LPL.arizona.edu

## Slide 12: Cold Lightweight Imagers For Europa (C-LIFE)
Main challenges: Planetary Protection
  6-log bioburden reduction required for the camera head, 4-log for the vault
  All parts have been verified to survive the bakeout times and temperatures required
Main challenges: Low available energy
  Mitigated with ConOPs and components that require no survival heating
  Detailed energy budget (and allowance from project) still TBD
Main challenges: Low Downlink Capacity
  600 Mbit for all science data in the mission (no instrument breakdown available)
  With a traditional campaign C-LIFE could take up to 2/3 of this.
  Smarter ways to select what to download will be investigated over the next year
Shane Byrne – shane@LPL.arizona.edu

## Slide 13: Cold Lightweight Imagers For Europa (C-LIFE)
Summary
Stereo color imaging with dual-periscope design
LEDs for imaging within shadows or at night
Strobing LEDs to excite fluorescence in organic material
No moving parts with progressive focus & strip filters
Highly radiation tolerant
No survival heating in nominal operations
Adopts the most stringent Planetary Protection protocols
Data filtering and compression accommodates low data rates and radiation-noise removal
C-LIFE is suitable for the surface of airless Ocean Worlds with little modification
Work continues on improving autonomy and fluorescence detection
Shane Byrne – shane@LPL.arizona.edu